## Slide 1: Flow-based Process: Intraday Capacity Calculation (IDCC)
Adrian Curtze-Rodriguez

## Slide 2: Agenda
Aim and goal of TSO regarding CrossZonalCapacities
Process overview DACC & IDCC
IDCC in detail
Publication locations
Key numbers and figures

## Slide 3: Aim and goal of TSO regarding CrossZonalCapacities
 | Core
 | Nordic
 | Further Bidding Zones
Accordance with CACM Regulation
Efficient Cross Border Allocation
Higher integration of national electricity markets
Simplified Capacity Calculation regions
IDCC process started on May 28th 2024
Intraday Capacity Calculation

## Slide 4: Process overview DayAheadCapacityCalculation and IntraDayCapacityCalculation
Starting from Day-Ahead Timeframe, a repetitive loop from Capacity Calculation, to Allocation and afterwards Security Analysis starts.
Core CCR Perimeter
External (MCSC, JAO..)
04:30
18:00 – 24:00
12:00 – 24:00
00:00 – 24:00

## Slide 5: IntraDayCapacityCalculation in detail
Process name | Used grid model | Updated timeframe | Provision of capacities to the market | Subsequent allocation process
IDCC(a) | D2CF | 00:00-24:00 | D-1 15:00 | IDA1 + Continuous trade
IDCC(b) | DACF | 00:00-24:00 | D-1 22:00 | IDA2 + Continuous trade
IDCC(c) | IDCF | 06:00-24:00 | D 04:30 | Continuous trade
IDCC(d) | IDCF | 12:00-24:00 | D 10:00 | IDA3 + Continuous trade
IDCC(e) | IDCF | 18:00-24:00 | D 16:00 | Continuous trade

## Slide 6: IntraDayCapacityCalculation in detail
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
Different to DayAhead
no minRam adjustment or LongTermAllocation inclusion

## Slide 7: IntraDayCapacityCalculation in detail
IDCC (b) as example
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
Critical Network Elements Contingencies
Required Inputs which are delivered
Common Grid Model
Generation and Load Shift Keys
Already Allocated Capacity
Allocation Constraints
External Constraints

## Slide 8: IntraDayCapacityCalculation in detail
IDCC (b) as example
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
Exchange AB
Exchange AC
1
2
3
4
5
6
7
CNEC | RAM | Fmax | FRM | Fi | IVA | PTDF A->B | PTDF C->D | PTDF E->F
1 | 800 | 1000 | 100 | 100 |  | 0,12 | 0,10 | 0,04
2 | 700 | 1000 | 100 | 200 |  | 0,15 | 0,12 | 0,20
3 | 600 | 1000 | 100 | 300 |  | 0,02 | 0,16 | 0,18
4 | 500 | 1000 | 100 | 400 |  | 0,3 | 0,25 | 0,2
5 | 500 | 1000 | 100 | 400 |  | 0,15 | 0,03 | 0,09
6 | 600 | 1000 | 100 | 300 |  | 0,18 | 0,09 | 0,21
7 | 700 | 1000 | 100 | 200 |  | 0,23 | 0,19 | 0,28
8 | 500 | 1000 | 100 | 400 |  | 0,01 | 0,03 | 0,02
9 | 500 | 1000 | 100 | 400 |  | 0,02 | 0,04 | 0,03
10 | 700 | 1000 | 100 | 200 |  | 0,01 | 0,04 | 0,04
11 | 600 | 1000 | 100 | 300 |  | 0,03 | 0,01 | 0,01
Only CNECs with PTDF >5% are used further

## Slide 9: IntraDayCapacityCalculation in detail
IDCC (b) as example
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
CNEC | RAM | Fmax | FRM | Fi | IVA | PTDF A->B | PTDF C->D | PTDF E->F
1 | 800 | 1000 | 100 | 100 |  | 0,12 | 0,10 | 0,04
2 | 700 | 1000 | 100 | 200 |  | 0,15 | 0,12 | 0,20
3 | 600 | 1000 | 100 | 300 |  | 0,02 | 0,16 | 0,18
4 | 500 | 1000 | 100 | 400 |  | 0,3 | 0,25 | 0,2
5 | 500 | 1000 | 100 | 400 | 100 | 0,15 | 0,03 | 0,09
6 | 600 | 1000 | 100 | 300 |  | 0,18 | 0,09 | 0,21
7 | 700 | 1000 | 100 | 200 |  | 0,23 | 0,19 | 0,28
Local Validation
  Due to the reduced timings in IDCC compared to DACC, in ID only a short local validation is possible (40 minutes max).
  Reminder Objective:
    Identify and apply measures for resolving the potential violation of operational security given by the flow-based domain results
Exchange AB
Exchange AC
1
2
4
5
6
3
7

## Slide 10: IntraDayCapacityCalculation in detail
IDCC (b) as example
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
1
2
4
5
6
3
7
Shift to the AAC
CNEC | RAM before AAC shift | Final RAM
1 | 800 | 750
2 | 700 | 650
3 | 600 | 600
4 | 500 | 550
5 | 400 | 450
6 | 600 | 650
7 | 700 | 700
Exchange AB
Exchange AC
Final Computation including shift to latest AACs
  During the IDCC process the Intraday market remains open and market participants can continue to trade.
  To ensure that the ID cross border trades that took place during the IDCC process are considered the Final FB domain is shifted to the “AAC” point, which stands for Already Allocated capacities

## Slide 11: IntraDayCapacityCalculation in detail
IDCC (b) as example
IDCC (b-e) process main steps
Initial delivery
Initial FB calculation
Validation
Final ATC extraction
Exchange AB
Exchange AC
1
2
4
5
6
3
7
CNEC | Final RAM
1 | 750
2 | 650
3 | 600
4 | 550
5 | 450
6 | 650
7 | 700
Border | ID ATC
AB | 400
BA | 450
AC | 300
CA | 350
ID ATC Extraction
ID ATC Domain
ID ATC AB
ID ATC AC
AAC
ATC Extraction
  Reminder: The ID market (both Continuous Trading on XBID as the ID auctions) are not compatible with FB domains. Thus, FB domains need to be converted to ATC/NTCs.
  This is done via an iterative algorithm that tries to extract the largest ATCs possible within the FB domain.  i.e. the rectangle should not go outside the FB domain.

## Slide 12: Information sources – JAO publication tool
https://publicationtool.jao.eu/coreID/

## Slide 13
Credit goes to Frank Boerman: https://data.boerman.dev/ & https://idcc.coreflowbased.eu/
Information sources

## Slide 14: Distribution of Hourly positive NTC increase via IDCC (b) in 2024
*only positive [NTC (b) - NTC (a)] values are taken into account